## Slide 1: Project GRAIL – Accelerating DBMS performance through latency masking hardware multithreading
Ildar Absalyamov, PhD Candidate
Advisors: Prof. Vassilis Tsotras, Prof. Walid Najjar

## Slide 2: Problem
Holy GRAIL of in-memory analytics:
Improving performance of analytical operations

## Slide 3: Our solution
Use Hardware Multithreading to mask memory access latency

## Slide 4: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA Implementations
Experiments
Conclusions & Future Work

## Slide 5: Motivation
Hardware landscape 2016:
  Gigabytes of RAM available on average server
  Issues of scaling algorithms on multicores
  Growing market for main-memory transaction processing & analytics

## Slide 6: Memory Wall
The biggest in-memory analytics bottleneck
[Hennessy and Patterson. Computer Architecture: A Quantitative Approach. 5th edition]

## Slide 7: Caches
CPUs mitigate memory latencies by using caches
Pros:
  Good abstraction
Cons:
  Increase power consumption
  Rely on data access locality
  “Leaking” abstraction: complicated algorithms
Caches, caches caches!

## Slide 8: Cache Misses: Bottleneck
Cache misses are major source of stall cycles for both analytical [TODS’07] & transactional workloads [DaMoN’13]
[DaMoN’13] Tözün, P. et al. OLTP in wonderland: where do cache misses come from in major OLTP components?
[TODS’07] Chen, S. et al. Improving Hash Join Performance through Prefetching

## Slide 9: Multithreading
Instantiating large number of threads
Fast thread context switching
Pros:
  Fully mask latency if enough threads are available
  General-purpose solution, does not rely on locality
  Simple “as if single-core” algorithms
Cons:
  Careful synchronization & scheduling
  Performance degrades if # of threads is low

## Slide 10: Multithreading: History
SPARC
  Limited only to 64(8x8) hardware threads
Cray(Tera) XMT
  Up to 128 threads, very custom high-end priced architecture
GPUs
  Rigid control flow limitations

## Slide 11: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA implementations
Experiments
Conclusions & Future Work

## Slide 12: Data Path: Custom vs. Generic
CPU Data path: too generic
  ICache misses
  DCache misses
  Branch mispredicts
Custom Data Path:
  Computation performed by 1 thread
  Hard wired digital circuit
    Pros: Small working state (ID of the stage in the pipeline + some data)
    Cons: hard to implement

## Slide 13: Hardware Multithreading Approach
Customized data path
  Application logic is a hardware circuit
Multithreading memory latency masking
  1000s of active threads
FPGA-based multithreading implementation
  Easy to prototype the approach

## Slide 14: FPGA Hardware Multithreading
Preempting executing thread once it access memory
Ready & Waiting Threads Queues on FPGA fit 1000s of thread states
ThreadM State
…
Ready threads
…
Waiting threads
Main memory
Memory
response
Memory
request
Data Path
Next
thread
Executed
thread
FPGA
Thread1 State
ThreadN State
Thread N’ State

## Slide 15: Hardware Multithreading: Use Cases
Algorithms with non-regular data access patterns:
  Hash Join
  Hash Group-by Aggregation
  Graph algorithms (out of talk’s scope)

## Slide 16: Main Assumptions
All data resides in memory
FPGA has direct access to the memory
Hash Table: traditional bucket-based
Coarse-grained synchronization: lock per bucket

## Slide 17: Thread Synchronization
Hash table-based algorithms: synchronization during build phase
Problem: need to push locking down to FPGA
Initial approach – use platform-specific memory locking
Better solution – use CAM (Content Addressable Memory) as synchronizing primitive
  CAMs allows single-cycle content-based lookup

## Slide 18: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA implementations
Experiments
Conclusions & Future Work

## Slide 19: Join Example: Build Phase
HT Bucket
Lock CAM
HashTable
Outstanding memory requests
Operation
Memory
FPGA
Create Node A
Build Relation: A C …

## Slide 20: Join Example: Build Phase
HT Bucket
Lock CAM
h(A)=𝛼
Outstanding memory requests
Operation
Bucket 𝛼
HashTable
Node A
Memory
FPGA
Create Node A
Update Bucket 𝛼
𝛼
Build Relation: A C …

## Slide 21: Join Example: Build Phase
Build Relation: A C …
HT Bucket
𝛼
Lock CAM
Bucket 𝛼
HashTable
Node A
Outstanding memory requests
Operation
Memory
FPGA
Create Node C
Update Bucket 𝛼

## Slide 22: Join Example: Build Phase
HT Bucket
𝛼
Lock CAM
h(C)=𝛼
Key | Bucket
C | 𝛼
Recycled jobs
Bucket 𝛼
HashTable
Node A
Node C
Outstanding memory requests
Operation
Memory
FPGA
Create Node C
Update Bucket 𝛼
Build Relation: A C …

## Slide 23: Join Example: Build Phase
HT Bucket
𝛼
Lock CAM
Bucket 𝛼
HashTable
Node A
Node C
Outstanding memory requests
Operation
Update Bucket 𝛼
Memory
FPGA
Key | Bucket
C | 𝛼
Recycled jobs
Build Relation: A C …

## Slide 24: Join Example: Build Phase
HT Bucket
Lock CAM
Bucket 𝛼
HashTable
Node A
Node C
Outstanding memory requests
Operation
Key | Bucket
C | 𝛼
Recycled jobs
Memory
FPGA
Update Bucket 𝛼
𝛼
Build Relation: A C …

## Slide 25: Join Example: Build Phase
HT Bucket
𝛼
Lock CAM
Bucket 𝛼
HashTable
Node A
Node C
Outstanding memory requests
Operation
Update Bucket 𝛼
Memory
FPGA
Key | Bucket
Recycled jobs
Build Relation: A C …

## Slide 26: Join: Probe Phase
For each tuple from Probe relation:
  Calculate hash value
  Probe Hash Table for linked list head pointer
  Search linked list for a match
  Output tuples which match

## Slide 27: Hash Join Bottlenecks
Main factors affecting join performance:
  Synchronization during build phase
    Assumption: Hash Table is built for smaller relation
    Worst case: relations have equal size
  Long linked list chains (e.g. heavily skewed data)
    Optimization: maintaining sorted order of linked list & early termination

## Slide 28: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA implementations
Experiments
Conclusions & Future Work

## Slide 29: Hash Group-by Aggregation: Differences
Single phase, synchronization always required
  E.g. no read-only phase
Search before adding a node
  Lock should be acquired earlier
Some temporal locality
  Depends on grouping key cardinality

## Slide 30: Aggregation: CAMs
Lock CAM maintains locks for hash table buckets which are searched, thus ensuring serialization
Filter CAM pre-aggregates tuples with the same grouping keys locally on FPGA
Notes: change the order of the CAMs?

## Slide 31: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
Lock CAM
h(A)=𝛼
Key | Count
Outstanding memory requests
FPGA
Memory
Operation
Key | Count
Hash Table
A
1
𝛼
Search A

## Slide 32: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
𝛼
Lock CAM
h(C)=𝛼
Key | Count
A | 1
Bucket 𝛼 locked by another thread
Key | Bucket
C | 𝛼
Recycled jobs
FPGA
Memory
Outstanding memory requests
Key | Count
Hash Table
Operation
Search A
C
1

## Slide 33: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
𝛼
Key | Count
A | 1
C | 1
Key A was not found
Insert new entry for A
Key | Bucket
C | 𝛼
Recycled jobs
FPGA
Memory
Lock CAM
Key | Count
Hash Table
Outstanding memory requests
Operation
Search A
Insert {A:1}

## Slide 34: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
Key | Count
C | 1
Key | Bucket
C | 𝛼
Recycled jobs
Lock CAM
Key | Count
Hash Table
FPGA
Memory
Outstanding memory requests
Operation
Insert {A:1}
𝛼
Search C

## Slide 35: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
𝛼
Key | Count
C | 
Key C locally aggregated
In Filter CAM
FPGA
Memory
Lock CAM
Key | Count
Hash Table
Outstanding memory requests
Operation
Search C
Insert {A : 1}
1
2
A
1

## Slide 36: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
𝛼
Key | Count
C | 2
FPGA
Memory
Lock CAM
Key С was not found
Insert new entry for С
Key | Count
A | 1
Hash Table
Outstanding memory requests
Operation
Search C
Insert {C:2}

## Slide 37: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
h(A)=𝛼
Key | Count
FPGA
Memory
Lock CAM
Key | Count
A | 1
Hash Table
Outstanding memory requests
Operation
Insert {C:2}
Search A
A
1
𝛼

## Slide 38: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
𝛼
Key | Count
A | 1
FPGA
Memory
Lock CAM
Key | Count
A | 1
Hash Table
Outstanding memory requests
Operation
Insert {C:2}
Search A
C
2

## Slide 39: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
𝛼
Key | Count
A | 1
FPGA
Memory
Lock CAM
Key | Count
A | 1
С | 2
Hash Table
Key A:1 was found
Update existing entry for A
Outstanding memory requests
Operation
Search A
Update {A:1+1}

## Slide 40: Aggregation Example
Grouping keys sequence : A C C A
Filter CAM
HT Bucket
Key | Count
FPGA
Memory
Lock CAM
Key | Count
A | 
C | 2
Hash Table
Outstanding memory requests
Operation
Update {A: 2}
1
2

## Slide 41: Hash Aggregation: Bottlenecks
Main factors affecting aggregation performance:
  CAM size: current design scales to 128 entries
    We explore alternative CAM designs which trades off size for speed (e.g. several-cycle lookup)
  Hash Table merge post-processing
    Function of cardinality, does not depend on data size

## Slide 42: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA implementations
Experiments
Conclusions & Future Work

## Slide 43: FPGA Engine Parallelism
Target platform: Convey-HC
  4 Xilinx Virtex 6 FPGAs x 16 Memory channels\FPGA
Designs
  Replicated join (4 chans/eng, 4 eng/FPGA)
  Replicated aggregation (4 chans/eng, 4 eng/FPGA)
  Multiplexed aggregation (2.5 chans/eng, 6 eng/FPGA)
Main Memory
..Memory channels..
1
2
15
16
Engine1
Engine4
Replicated Engine Design
Main Memory
..Memory channels..
1
2
15
16
Engine1
Multiplexed Engine Design
Engine2
Multiplexed Engines
…
…
Notes: !!!!!!Mention merging!!!!!!

## Slide 44: Software Comparison
5 aggregation algorithms
  Independent Tables
  Shared Table
  Partition & Aggregate
  Hybrid Table
  Partition with Local Aggregation Table
[ICDE’13] Balkesen, C. et al. Main-memory Hash Joins on Multi-core CPUs: Tuning to the underlying hardware.
[VLDB’07] J. Cieslewicz et al. Adaptive Aggregation on Chip Multiprocessors.
[DAMON’11] Y. Ye et al. Scalable aggregation on multicore processors
Hardware-oblivious [VLDB’07]
Hardware-conscious [VLDB’07]
Hybrid [DAMON’11]
2 join algorithms
  Non-partitioned
  Partitioning-based
[ICDE’13]
Hardware-oblivious
Hardware-conscious

## Slide 45: Experiments: “Skinny” Tables
Columnar data format with two 4-byte wide fields:
  32bit primary key
  32bit payload(grouping key)
Distributions: Unique, Uniform(Random), Heavy Hitter, Moving Cluster, Self Similar, Zipf
Relation sizes 1M to 1B
Grouping key cardinalities 1K to 4M

## Slide 46: Experiments: TPC-H
Schema from TPC-H benchmark
Only join between Orders & Customers tables (no projections\selections yet)
  Part of Q3, Q5, Q7, Q8, Q10, Q13, and Q18
Always probe-dominated
Scale factors from 1 to 10

## Slide 47: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA implementations
Experiments
Conclusions & Future Work

## Slide 48: Join: Unique Throughput
2x

## Slide 49: Join: Uniform Throughput
3x

## Slide 50: Join: Scale Up (Probe Dominated)
Each 4 CPU threads vs. 1 FPGA (roughly matches memory bandwidth)
4x

## Slide 51: Join: Worst Case Scale Up |R|=|S|
2x

## Slide 52: Join: Normalized Throughput
4x

## Slide 53: Join: TPC-H Throughput
Orders ⋈custkey Customer
1.5x

## Slide 54: Aggregation: Self Similar Throughput
10x

## Slide 55: Aggregation: Final Merge Effects
Merge
Overhead
8M
Merge
Overhead
128M
Merge operation introduces a constant overhead, which diminishes as relation grows

## Slide 56: Aggregation: Bandwidth Utilization
FPGA implementation achieves much higher memory bandwidth utilization

## Slide 57: Outline
Motivation
Hardware Multithreading Approach
Use Cases
  Hash Join
  Hash Aggregation
Software & FPGA implementations
Experiments
Conclusions & Future Work

## Slide 58: Conclusions
Implemented an FPGA-accelerated hash join by aggregation operator [CIDR’15]
Proposed an FPGA-accelerated hash group by aggregation operator [DaMoN’16]
Explored CAMs as a pre-aggregation cache & synchronization primitive [DaMoN’16, ICCAD’15]
[CIDR’15] Halstead, R. et al. FPGA-based Multithreading for In-Memory Hash Joins.
[ICCAD’15] Windh, S. et al. CAMs as Synchronizing Caches for Multithreaded Irregular Applications on FPGAs
[DaMoN’16] Absalyamov, I. et al. FPGA-accelerated group-by aggregation using synchronizing caches.

## Slide 59: Future Work
Implement other relational operators to build fully-fledged query processor
Explore tradeoff between CAM size vs. speed
Apply hardware multithreading to transactional workloads (e.g. implement CAM-based concurrency control)

## Slide 60: UCR Team
Prof. Walid A. Najjar
Prof. Vassilis J. Tsotras
Robert J. Halstead
Prerna Budhkar
Skyler Windh

## Slide 61: Questions?

## Slide 62: Backup slides

## Slide 63: Experimental Evaluation
Four synthetically generated datasets with varied key distribution
  Unique: Shuffled sequentially increasing values (no-repeats)
  Random: Uniformly distributed random values (few-repeats)
  Zipf: Skewed values with skew factor 0.5 and 1
Each dataset has a set of relation pairs (R&S) ranging from 1M to 1B tuples
Results were obtained on Convey-MX heterogeneous platform
Hardware Region | 
FPGA board | Virtex-6 760
# FPGAs | 4
Clock Freq. | 150 MHz
Engines per FPGA | 4 / 3
Memory Channels | 32
Memory Bandwidth (total) | 76.8 GB/s
Software Region | 
CPU | Intel Xeon E5-2643
# CPUs | 2
Cores / Threads | 4 / 8
Clock Freq. | 3.3 GHz
L3 Cache | 10 MB
Memory Bandwidth (total) | 102.4 GB/s

## Slide 64: Throughput Results: Zipf_1.0 dataset
FPGA throughput decreases significantly due to stalling during probe phase

## Slide 65: FPGA Implementation: Build Phase Engine
Every cycle a new tuple enters the FPGA engine
Every tuple in R is treated as a unique thread:
  Fetch tuple from memory
  Calculate hash value
  Create new linked list node
  Update Hash Table
    Has to be synchronized via atomic operations
  Insert the new node into the linked list
Notes: Robert: does the link list append use atomic operation? (no, the HT request does an atomic read/update operation. Whatever is read goes to the linked list update.)

## Slide 66: FPGA Implementation: Probe Phase Engine
Every tuple in R is treated as a unique thread:
  Fetch tuple from memory
  Calculate hash value
  Probe Hash Table for linked list head pointer
    Drop tuples if the hash table location is empty
  Search linked list for a match
    Recycle threads through the data-path until they reach the last node
  Tuples with matches are joined
Stalls can be issued between New & Recycled Jobs

## Slide 67: FPGA Area & Memory Channel Constraints
Target platform: Convey-MX
  Xilinx Virtex 6 760 FPGAs
  4 FPGAs
  16 Memory channels per FPGA
Build engines need 4 channels
Probe engines need 5 channels
Designs are memory channel limited